## Slide 1
TABLE Nine
MACMIO
MIDI and Audio Control with Multiple Input and Output
Coding
Packaging
Abstract:
The purpose of our project is to create an easy-to-use music player to be implemented in the Longmont SmartHome. It will allow the residents there to both listen to and play along with their favorite music, encouraging creativity and fun.
The MACMIO will be able to produce sounds using a synthesizer code called Mozzi. It will also be able to send MIDI signals to a computer which can be easily modified to make different effects.
Design Process:
Circuitry
Acknowledgements: We would like to thank Tim May and Doug Walter for helping us with our circuitry. We also want to thank our TAs: Madison and Katelyn.
Timeline
Materials and Budget
Our Client:
Stacey is our client at Imagine! CO. She lives in the Longmont SmartHome and loves music, so we are making a device which will let her play along to her favorite songs.
How it Works:
Plays 5 songs from an SD card
Allows the user to play sound effects over the music
5 buttons for sound effects and a slider to change the pitch of the effects
Volume is controlled with a proximity sensor
Sound effects can be produced by connecting the box to speakers or by connecting to a computer
Uses two Arduino Redboards and an Mp3 Trigger
Circuitry array is connected to a 12 volt power supply.
Slider
Big Button
Small Buttons
Proximity Sensor
Mp3 Trigger
Mozzi Redboard
Non-Mozzi Redboard
External Speaker
Computer
Midi
Button Panel
LED Strip
Power Supply 12 Volt
9 Volt Regulator
Mozzi Arduino
MIDI Arduino
MP3 Trigger
Proximity Sensor
Slider
Servo
Audio Mixer
MIDI to USB
Power
Circuit Connections
We have two sets of code- one for each Arduino. One exclusively controls Mozzi. The other handles MIDI signals (including the slider) as well as volume.
This is how the box was assembled. We used a laser-cutter to make teeth as well as the holes for the various controls. Inside, the different boards and controls were bolted in. There is an access panel on the bottom for changing out the SD card.
GEEN 1400-50 Piket-May
MIDI
“MIDI” is the name of a protocol which is used for music. Components can be programmed to send MIDI to a computer. The computer can then use a program such as Audacity or Garageband to take those signals and turn them into sounds.
Mozzi
We needed to produce sounds directly from the Arduino processor. After research, we found a library of synthesizer effects for Arduino called “Mozzi.” We picked effects that we liked and modified their code to actuate with a button.
Boards | $101.33
Control Surfaces | $36.50
Servo Apparatus | $41.64
Power Supply | $46.95
Mixer | $22.39
Acrylic | $25.95
Misc. Costs | $87.18
Total | $361.94
This large button will cycle through 5 songs.
These small buttons play sound effects.
This missile switch turns on the box.
This slider changes MIDI sound effects.
This proximity sensor uses a servo to change to volume of all sounds.
Using the MACMIO